## Slide 1
Einstein Telescope Site Evaluation Parameters WG3 working group
Stefano Cuccuro, Alain Dassargues, Riccardo DeSalvo, László Kovács, Giovanni Losurdo, Aniello Grado, Maria Marsella, Frédéric Nguyen, Giacomo Oggiano, Andrea Paoli, Wolfango Plastino, Peter Van, Dorota Rosinska

## Slide 2
Purpose of the Site Evaluation Parameters (SEP) WG3 is to define the site evaluation parameters from an infrastructural and geological point of view. This should include all the possible parameters that have an impact on:
Infrastructure cost
Detector operation
Detector lifetime
Safety
The output is a document
SCOPE

## Slide 3: WG3 doc organization
                Detector requirements
General list of site parameters
              Surface
                Underground
                Safety
                lifetime
Detailed list (with context/description)
Info/lesson learned from other surface/underground facilities

## Slide 4: Science driven requirements
Requirement | 
Lifetime | 50 years
Topology | Δ/L
Detector depth | Few 100 m (we need input)
Seismic noise | ? (at the three detector corners)
Earthquakes frequency | ? (impact on duty cycle)
Tunnels/caverns stability | ?
Caverns size | ?
Vacuum pipe diameter | 1.2m ?
Number of pipes in the tunnel | 4?
Pipe material | STS 304L ?
Lot of work done for ET but some parameters need to be frozen

## Slide 5: Surface
Surface
Analysis of surface conditions
Land use
ground stability DinSAR
Interference analysis
Analysis of descendery portals
….
…..
Notes: Differential Interferometric Synthetic Aperture Radar

## Slide 6: Underground
Rock mechanics
Determine position of dislocations and faults
Rock mass classification
Strength parameters
Elastic parameters
Anelastic parameters
Constitutive model of rocks
Distribution of rock stresses

## Slide 7: Underground
Hydrology
Hydraulic conductivity
Porosity
Effective drainage porosity
Dispersivity coefficients
Water table location
Constitutive model of rocks
Distribution of rock stresses
Hydrogeological data must be collected corresponding to the different lithological faces (i.e. nature of the geological formations) that can be potentially encountered according to the different possible configurations of the ET.

## Slide 8: Safety
Safety
Radioactivity
Radon
Thoron
Water inrush
EURATOM establishes reference levels for indoor radon concentration -> 100 Bq m-3
Measurement of radon and thoron are needed underground and outside (radon can enter through ventilation system).
Radon can enter through groundwater
Selection of construction materials needed
Notes: Gran Sasso Labs are equipped with diving masks and diving cylinder

## Slide 9: Lifetime
Corrosion | 
Umidity | 
pH | 
Chemicals | STS particularly sensitive to Chloride
MIC (Microbiologically Influenced Corrosion | X100 faster corrosion
AC-induced corrosion | high voltage electric power lines or in AC-powered railway systems induce electromotive forces into vacuum pipelines
The detector lifetime should be of the order of 50 years
A corrosion plan should be adopted

## Slide 10: Experience from other surface/underground scientific facilities
In the Doc we have a section where to report
Info and lesson learned from other surface/underground facilities

## Slide 11: CERN
Some preliminary info from CERN:
Tunnel diameter 4m
Depht: 80-140 m
They had a quite stringent requirement on the ground stability due to the necessity to keep well aligned the accelerator pipe (0.1 mm accuracy)
they have a ventilation of 1 vol/hour, this is enough to keep the humidity under control
temperature: 17-18 ℃
dew point: 12 ℃
they had some corrosion problem with bellows due to chlorides and to the cryogenic system (much thicker STS ) due again to chloride residuals .

## Slide 12
SEP
Differences among sites will translate in additional costs and longer realization time.
Difference among sites will affect the detector performance
COST PARAMS
PERFORMANCE PARAMS

## Slide 13: Sites comparison
Costs params:
A reasonable approach is to ask specialized companies to make a detailed design that includes a risk management plan
Performance params:
Done by people involved in detector design (with feedback from civil engineers)

## Slide 14: ET underground infrastructure cost assessment requires a risk management plan
Includes:
Rockburst in hard rock
Deformations on soft rock
High pressure mudflow
Water inrush
Including epistemic and aleatory uncertainty
J.A. Hudson, X. Fend – Rock Engineering Risk CRC PRESS 2015

## Slide 15: ET underground infrastructure cost assessment requires a risk management plan
Identify lithology
Identify tectonic condition
Local geological structures
Estimation of full in situ stress tensor
Hydraulic conductivity
Porosity
Drainage porosity
Strong scale effect

## Slide 16: Variability of geological conditions can lead to squeezing behaviour

## Slide 17: LEP TUNNEL
exploration tunnel about
4 km long to explore the
transition from the molasse to limestone
2 years program of test borings: 9 km vertical boreholes (including one 1000m deep)
Extensive geological and hydrological studies
Problems under the Jura Mountain due to water inrush and mudflow with delay of 8 months and cost increase

## Slide 18: Conclusion
To compare the infrastructure cost among sites a detailed design is needed that includes geological/hydrogeological detailed investigations and a risk management plan.
Underground seismic sites characterization at the foreseen location of the three detector corners to take into account small scale effect due to lithostratigraphic variation

## Slide 19: ET roadmap
TIMING

## Slide 20: TIMING
Site qualification early 2021 !!
First WG3 doc draft before summer break
Geological and hydrogeological campaign (~ 2 years ?)
  In case of detailed design done by specialized companies, should campaigns be made by the companies ?
Seismic sites characterization at the foreseen detector corners (~ 1 year ?)

## Slide 21
THANKS