## Slide 1
ET Site evaluation
WG2 group
status report
June 13, 2019

## Slide 2
ET Site evaluation
SEISMIC
ACOUSTIC
MAGNETIC

## Slide 3
SEISMIC
What to measure:
ambient noise;
Newtonian noise;
background seismicity;
effects of large regional and tele-seismic earthquakes;
…
Seismic percentile at Virgo site
Note: at least one year of data-taking ?

## Slide 4
SEISMIC
What to measure:
ambient noise;
Newtonian noise;
background seismicity;
effects of large regional and tele-seismic earthquakes;
…
Installation Best Practice:
Far from sources of local noise (fans, cars, equipment, plants);
Good cohesion with bedrock;
Shielding from air circulation and thermal variation.
Sealed steel isolation chamber with 4-inch thick base plate
STS-2 seismometer and its thermal insulation

## Slide 5
SEISMIC
What to measure:
ambient noise;
Newtonian noise;
background seismicity;
effects of large regional and tele-seismic earthquakes;
…
Installation Best Practice:
Far from sources of local noise (fans, cars, equipment, plants);
Good cohesion with bedrock;
Shielding from air circulation and thermal variation.
Advices:
Good deployment prevents to record the installation noise and mask the true seismic signal
Costs:
~25k euro + site preparation.
Typical underground seismic station installation

## Slide 6: SOUND
What to measure:
acoustic noise over time at surface;
underground reverberation time of caverns (RT-60) by exploding fire crackers.
Typical spectra: underground (blue) and into the Virgo Laser Lab (red)
RT60 reverberation time measurement

## Slide 7: SOUND
What to measure:
acoustic noise over time at surface;
underground reverberation time of caverns (RT-60) by exploding fire crackers.
Installation Best Practice:
Protection against direct water and wind, mandatory;
Source of turbulence in the vicinity to be avoided;
Wind noise reduction via porous fabric domes recommended;
Long term deployments.
Infrasound microphone and its wind shielding.

## Slide 8: SOUND
Recommended instrumentation
Wide range infrasound microphone (0.1Hz-10kHz), with low inherent noise and good sensitivity;
Post-processing unit.
Costs:
~ 22 K euro per complete station; (digitizer ~10k euro could be shared with one seismometer).
Note: pairs of microphones at ~0.5 m could be useful to remove wind effect ? TBC
Typical sound microphone and electronic post-processing unit

## Slide 9
MAGNETIC
What to measure:
Schumann Resonances (SR) in the 8-60Hz range with intensity of [0.1-1] pT;
Lightning magnetic disturbance in the [0-few] kHz range;​
(underground) effect of rock magnetic properties on magnetic fields.​
Typical magnetic spectra
nT

## Slide 10
MAGNETIC
E-W component of a triaxial magnetometer getting buried.
What to measure:
Schumann Resonances (SR) in the 8-60Hz range with intensity of [0.1-1] pT;
Lightning magnetic disturbance in the [0-few] kHz range;​
(underground) effect of rock magnetic properties on magnetic fields.​
Installation Best Practice:
Surface sensors buried by ~0.5 m;
Use three mono-axis instruments to record the whole field;​
Prevent water or immersion;
Long distance from electronics and power supply;
Each of the tern should be at least 2m apart.
Recommended instruments:
LEMI-120 or Metronix MFS-06;
Broadband [1mHz – 1kHz] or [10Hz – 10kHz];
Sensor noise should be 10 times lower. (~.01 pT).
Cost:
3 x 6k euro (magnetometer) + 6k euro (digitizer).

## Slide 11
Summary Table
Observable | type | manufacturer | instrument | Cost (€) | Notes
SEISMIC | broadband | Streckeisen | STS-2 | Not available anymore | 
 | broadband | Streckeisen | STS-2.5 |  | 
 | broadband | Nanometrics | TH120 (Horizon) | 15k | 
 | broadband | Nanometrics | T240 | Not available anymore | 
 | broadband | Nanometrics | T360 | 45k | 
 | geophone | Geotech | GS-13 | 8k | 
 | geophone | Sercel | L4C | 2k | 
 | broadband | Streickeisen | STS-5A |  | borehole
 |  | Geotech | KS-5400 |  | borehole
 |  | Nanometrics | Trilium 120 BH |  | borehole
MAGNETIC | magnetometer | Metronix | MFS-06 | 6k | 
ACOUSTIC | microphone | BKSV | B&K 4193 | 2k | 
 | preamp | BKSV | Nexus | 10k | 
-------------- | -------------- | -------------- | -------------- | -------------- | --------------
 | datalogger | Quanterra | Q330 + recorder | 10k | 
 | datalogger | Nanometrics | Centaur | 6k | 

## Slide 12
ET Site evaluation
Thank you for your attention
END