## Slide 1: AEI-SAS and Control with blended sensors
26.04.2013
Conor Mow-Lowry
For the 10m prototype team
March 2014
GEO ISC

## Slide 2: Seismic Attenuation System
Optical table with 1.75 m side length
Low-frequency seismic isolation from 0.1Hz
Ultra high vacuum compatible
Natural frequencies:
  Tilt: ~450 mHz
  Horizontal: ~100 mHz
  Vertical: ~250 mHz
Maximum (forced) seismic isolation:
  Vertical: 60 - 80 dB
  Horizontal: 70 - 90 dB
ø3000
3200
2000
[mm]
Volume: ~25 m³

## Slide 3: Simplified representation
Optical table
Filter support
Base plate
Inverted pendulum
legs
Geometric anti-spring filters

## Slide 4: Horizontal Isolation
Optical table
Filter support
Base plate
P-wave
Particle motion
Love wave
Particle motion
www.geo.mtu.edu/UPSeis/

## Slide 5: Vertical Isolation
Optical table
Filter support
Base plate
www.geo.mtu.edu/UPSeis/
S-wave
Particle motion
Particle motion
Rayleigh wave

## Slide 6: Height Reduction
Optical table
Filter support
Base plate

## Slide 7: Height Reduction I
Optical table
Filter support
Base plate

## Slide 8: Height Reduction II
Optical table
Filter support
Base plate

## Slide 9: Sensors & Actuators
Seismometer
3 horizontal sensor/actuator pairs
3 horizontal motorized springs
4 vertical motorized springs
3 vertical sensor/actuator pairs
3 vertical commercial geophones
3 horizontal custom made
monolithic Accelerometers
Notes: Inertial sensors – table motion
Displacement sensors - relative table position

## Slide 10: Table assembled

## Slide 11: Vertical spectrum in vacuum
[m/rtHz]

## Slide 12: Horizontal spectrum in vacuum
Mention on table, not replicated yet

## Slide 13: Control
Initially conservative (damping and DC only), now conceptually similar to the HAM-ISI control scheme
Vertical blending at 0.01 and 0.30 Hz
Horizontal blending at 0.04 and 0.15 Hz
Vertical U.G frequencies ~5-15 Hz
Horizontal U.G frequencies ~0.5-2 Hz
Notes: LVDTs + ground STS2 make a corrected sensor down to ~10mHz
Vertical geophones measure inertial motion directly on the table, only good above ~0.3Hz
Horizontal accelerometers are extremely good at low-F, but suffer tilt on spring-box and not sensitive enough above ~10 Hz
Vertical blend ~0.01 Hz and 0.3 Hz
UGF ~ 5-15 Hz
Horizontal ~ 0.04 Hz and 0.15 Hz
UGF ~ 0.5-3 Hz
Geophones add noise at ~30-100mHz

## Slide 14: Control
Notes: LVDTs + ground STS2 make a corrected sensor down to ~10mHz
Vertical geophones measure inertial motion directly on the table, only good above ~0.3Hz
Horizontal accelerometers are extremely good at low-F, but suffer tilt on spring-box and not sensitive enough above ~10 Hz
Vertical blend ~0.01 Hz and 0.3 Hz
UGF ~ 5-15 Hz
Horizontal ~ 0.04 Hz and 0.15 Hz
UGF ~ 0.5-3 Hz
Geophones add noise at ~30-100mHz

## Slide 15: Control
Notes: LVDTs + ground STS2 make a corrected sensor down to ~10mHz
Vertical geophones measure inertial motion directly on the table, only good above ~0.3Hz
Horizontal accelerometers are extremely good at low-F, but suffer tilt on spring-box and not sensitive enough above ~10 Hz
Vertical blend ~0.01 Hz and 0.3 Hz
UGF ~ 5-15 Hz
Horizontal ~ 0.04 Hz and 0.15 Hz
UGF ~ 0.5-3 Hz
Geophones add noise at ~30-100mHz

## Slide 16: Transmissibility in vacuum (Z)

## Slide 17: Transmissibility in vacuum (X)

## Slide 18: Inter-table motion with the SPI
Interferometrically measures table separation
Very low noise at low frequency
Uses an Iodine stabilised laser
Mach-Zender interferometers
Readout with LISA-pathfinder phasemeters

## Slide 19: Controlled spectra in vacuum

## Slide 20: Remaining work
Must do:
Install motorized springs
Create control initialisation algorithim, and safe fallback configurations.
At this point can install suspended optics – all going well in a few working weeks – late Oct/Nov.
Want:
Strengthen actuators
Test with STS2 on table
Improve vertical sensors
6x6 and/or freq-dependent matricies
Lower LVDT range (+/-1mm) and noise (factor of 10-50)
Functional minimum
  Install and test the remaining motorised springs
  Create start-up and fail-safe scripts for use with suspended optics, hopefully by early November
Performance upgrades
  Strengthen actuators to increase range and U.G frequency
  Test performance with accelerometers on table-top
  Optimise loop gains and blend frequencies
  Implement 6x6 and/or frequency dependent sensing and actuation matrices
Pipe dreams
  Improve vertical sensors
  Reduce LVDT range to +/-1mm, 10x less noise.

## Slide 21: Thank you for your attention!
Ken Strain: Scientific leader (Glasgow)
Harald Lück: Co-ordinator (Hannover)
  Tobin Fricke: Reference cavity, CDS, electronics
  Conor Mow-Lowry: Seismic isolation, suspensions, single-arm test
  Vaishali Adya: Interferometric sensing & control and simulations
  Gerald Bergmann: Isolation tables
  Manuela Hanke: Reference cavity
  Sina Köhlenbeck: Suspension Platform Intererometer, Single-arm test
  Tobias Westphal: Non-SQL suspensions, Thermal noise interferometer
Sean Leavey, Stefan Hild: Simulations and interferometric readout (Glasgow)
Gerrit Kühn: Real time control and data system
Andreas Weidner: Electronics and Electrical design
Benno Willke, Jan Hendrik Pöld, Patrick Oppermann: High power laser system
Liam Cunningham, Russell Jones, Alan Cumming, Giles Hammond: SQL IFO suspensions
Kasem Mossavi: Vacuum system and pumps control
Fumiko Kawazoe: Frequency reference cavity
  Thimotheus Alig , Alessandro Bertolini, Michael Born, Yanbei Chen, Katrin Dahl, Stefan Danilishin, Stefan Goßler, Christian Gräf, Sabina Huttner,Kentaro Somiya, Bob Taylor, Alexander Wanner
http://10m-prototype.aei.uni-hannover.de

## Slide 23: Geometric anti-spring filter
Expanded
Compressed
Anti-spring reduces the effective spring constant
with length l0x of the free spring and contraction x0 at the equilibrium

## Slide 24: Geometric anti-spring filters
Expanded
Compressed

## Slide 25: Passive isolators in GW detectors
TAMA-SAS
HAM-SAS
AEI-SAS
EIB-SAS
Notes: HAM-SAS used as guideline
Downscaled
Redesigned

## Slide 26: Part 4: Performance evaluation