## Slide 1: How the servo for the longitudinal control of the reference cavity was designed at the AEI 10 m Prototype
Fumiko Kawazoe, for the AEI 10m Prototype
GEO-isc meeting, 2012.03.28, Wendsday afternoon

## Slide 2: Contents
Requirement : why we need very high gain for the servo
How we designed the servo : Step 1 to Step 3
How we will convert the design into a real electronic circuit

## Slide 3: Overall layout
11 m
Sufficient spatial mode filtering
Triangular cavity (two flat mirrors and a curved mirror)
0.3 m
Notes: *It is a triangular cavity consisting of two flat mirrors and a curved mirror.
Two flat mirrors are located close together, (the distance between them is 0.3m) and the curved mirror is located ~10m away from the flat mirrors.
The cavity has an optical path length of ~20m.
*Parameters. (* TEM higher-order modes up to a certain modes, is suppressed by 1000…)
*Figure shows the overall layout of the reference cavity.
The laser beam is sent into the vacuum tank through a fiber.
The fiber and a Pre-Mode-Cleaner will give sufficient spatial mode filtering.
Part of this spatially filtered beam will be sent into the reference cavity.
All the detection systems will be placed on the detection bench located outside the vacuum tanks.

## Slide 4: Requirement from the sub SQL IFO
Sub-SQL noise budget
Common Mode rejection
ratio: 1%
Safety margin ~10
Notes: Total classical noise (TCN) should not be limited by laser frequency noise.
Setting TCN as upper limit for now, taking 1% of common mode rejection into account, and
Adding a safety margin of about 10.

## Slide 5: Comparison
Ref.Cav. sensitivity v.s. NPRO free running noise
2~3 orders of magnitudes more gain
20 Hz to 1k Hz
Notes: 2 to 3 orders of magnitudes of more suppression is required, ranging from 20 Hz to 1kHz.

## Slide 6: Design sensitivity
Ref.Cav. Noise budget (selected)
Optimize each noise so that
Total noise meet the target
Notes: Those noise sources that are relatively big are selected.
By optimizing each noise source, the total noise level (black dot) is designed just to meet the garget level(red).

## Slide 7: Control Topology
Frequency follows cavity lengh
additional phase lag (EOM driver, and post-mixer filters), that cannot be accurately predicted at this design phase and will cause problems, (Glasgow experience 1 MHz UGP with ~10m delay and 12 MHz modulation))
NPRO free running noise
Total noise
Target level
Max. gain: 107
fug=1 M Hz  fug=250 kHz
Initial design
Ratio
Noise : DC to high frequency
Covering all frequencies to avoid noise couplings( c.f. specification given from 20Hz to 1kHz)
Very high gain at DC guarantees cavity is locked very tightly (rms sense)
Notes: Although the target level is specified from 20Hz to 1kHz, in order to avoid noise couplings, we cover all the frequencies.
Using the PDH method, the laser frequency is forced to follow the cavity length. We can , if necessary to make it even better, at very low frequency
Set the Iodine laser that is used for the SPI system as the reference.
By taking the radio between the total noise level and the NPRO free running noise level, the gain that is needed for the servo is roughly calculated.
BUT
The unity gain frequency aimed at needs to include some safety
margin because additional phase lag will arise from electronics, for example photo detectors,
EOM driver, and post-mixer filters, that cannot be accurately predicted at this design phase.
If we set the unity gain frequency at 1MHz, the phase lag would be 40 degree , plus some others (probably not yet modelled) from the photodiode circuit, from the mixer low pass filter and from the EOM driver, will make it very hard to reach 1 MHz (At Glasgow they found it very hard to obtain good performance with 1 MHz UGP with ~10m delay and 12 MHz modulation)
So.
We aim at 250 kHz for the unity gain frequency at which the designed servo phase lag is less
than 10 degrees.
ALSO.
Having a very high gain at DC it would guarantee that the cavity is locked very tightly in an rms sense.

## Slide 8: Phase lag optimization
Shorten optical length between the laser(actuation point) and the PD(sensing point)
 | Physical length | Index of refraction
Input bench | 2.7 | 1
fiber | 6 | 1.5
Fiber headRef.cav. | 2 | 1
Ref.cav. PD | 3 | 1
PD Electronics | 5 | 1.5
Electronics Laser | 6 | 1.5
Total optical length | 33.2m | 
Phase lag at fug=250 kHz <10 °
Drawing of the Prototype hall
Notes: To optimize this phase lag…the optical path length is designed to be as short as possible.

## Slide 9: Step1: Designing the overall gain
A block diagram
Take TEMP feedback from after PZT gain
Changes to PZT gain do not need consequential changes to TEMPgain to maintain crossover stability.
Recommendation from Glasgow.
Check important numbers
Notes: By taking the TEMP feedback from after the PZT gain stage- that way TEMPgain can be very simple and changes to PZT gain do not need consequential changes to TEMPgain to maintain crossover stability. At Glasgow they have found this very convenient in practice.

## Slide 10: Step2:Build the model in Matlab
Based on a model used for a loop at Glasgow.
  Only use some standard GEO accessory functions written by Stuart Killbourne 1993
    lospass : low pass filter
    res2pole : resonant 2-pole low pass filter
    transint : transistional integrator
    transdif : transistional differentiator
Optimizing gain distribution when stacking them together to realize a realistic design.
Export it as a number of blocks (I use ss) into Simulink
Notes: For this I used a model that was used for a loop at Glassgow and modified each part.

## Slide 11: Step3: Do the Analysis with Simulink
Specify input and output,
Open-loop of closed loop,
Bode plot it.
Notes: build the model in MATLAB ,
2) export it as a number of blocks (I use ss) into Simulink
3) use Simulink to do the analysis (Control and Estimation Toolbox)
You can specify the input and output, open-loop or closed, Pronunciation :Boh-dee

## Slide 12: Optimizing cross over condition
Overall gain and each gain
Frequency[Hz]
Gain [dB]
Phase[deg.]
Frequency [Hz]
The relative slope f
Thanks to TEMP feedback from after PZT gain , optimizing cross-over condition became MUCH easier!
Notes: The relative slope f to the power of 1

## Slide 13: Building an electronic(on going)
Based on Simulink model build a Liso file
Optimise each component (e.g. op-amp output voltage < device’s limit,… )
Find the Op-amp that meets your gain requirement, slew-rate problems for practical electronics …(rather: when making a model, already use a realistic Op-amp model.)
…
Notes: Once these steps are done,

## Slide 14: Summary
Sub SQLRequirement(10^−4 Hz/ sqr Hz at 20Hz
rolling off to below 6 × 10^−6 Hz/sqrt Hz above 1 kHz)
Build a model and analyse (Matlab + Matlab Simulink)
Realize the model (Liso)

## Slide 15
FOR
YOUR
ATTENTION!
Notes: Send the file to dmitry.
Where does the 1000 come from, for the higher order modes?  Stefan H.