## Slide 1: FDTD Simulation of Diffraction Grating Displacement Noise
Daniel Brown
University of Birmingham
AEI, Hanover - 14/12/2010

## Slide 2: Overview
Motivation: Diffraction grating displacements
Finite-Difference Time-Domain(FDTD)
  Why use FDTD?
  How it works
  What problems there are
Measuring the Gaussian beam diffraction phase noise
Modelling the transmission on waveguide coatings
Conclusion

## Slide 3: Project Aim
Try and simulate phase noise[1] from moving diffraction grating.
  Simulate using a finite grating size using Gaussian beams
Implement and verify a 2D/3D FDTD numerical solver for Maxwell’s equations, this should be able to…
  Measure reactions to impulsive inputs like moving gratings/sources
  Simulate time-domain interaction of Gaussian laser beams with gratings
[1] A.Freise et al. Phase and alignment noise in grating interferometers.
New Journal of Physics 2007

## Slide 4: The phase noise
What are we looking for:
Additional phase periodic with grating period
Increase’s with diffraction order linearly
Linear relationship to the grating displacement
A.Freise et al. Phase and alignment noise in grating interferometers.
New Journal of Physics 2007

## Slide 5: Phase noise in a cavity
Allows for an all reflective component optical cavity[1]
Of particular use in GW detectors
Potential to reduce thermal disturbances compared to transmissive optical cavity
But, we see additional phase noise added on each reflection from the grating due to any lateral movements[2]
[1] K. Sun et al. Byer. All-reflective Michelson, Sagnac, and Fabry-Perot interferometers based on grating beam splitters.
[2] J Hallam et al. Lateral input-optic displacement in a diffractive Fabry-Perot cavity 2010

## Slide 6: Previous and ongoing work
Previous and ongoing work in Birmingham, Glasgow, Hannover and Jena
Experimental work in Birmingham attempting to measure effects of this phase noise
Previous work done at Birmingham by Daniel Wolliscroft on Transmission Line method for simulating EM propagation[1]
[1] Daniel Wolliscroft. Visualising the effects of mirror surface distortions, 2009
School of Physics and Astronomy, University of Birmingham

## Slide 7: Finite-Difference Time-Domain
Is an accurate and well proven solver of Maxwell’s equations in the for many different applications
Can solve Maxwell’s equations exactly, of course in reality numerical problems stop this

## Slide 8: Finite-Difference Time-Domain
…also been used for the very small, such as in photonics and nanophysics(waveguides and circular resonators)

## Slide 9: Finite-Difference Time-Domain
Need to solve Maxwell equations to simulate propagation of EM waves
Need to be able to simulate complicated problem spaces(i.e. various
Faraday and Ampere’s laws are only really needed for the simulation

## Slide 10: Finite-Difference Time-Domain
Expand Faraday and Ampere laws
Change in time of each fields component is dependant on only the other field and it’s previous value
Ignoring magnetic and current sources here

## Slide 11: Finite-Difference Time-Domain
The Yee Algorithm(1966)
  Defined the Yee Grid
Taflove, Allen and Hagness, Susan C. Computational Electrodynamics: The Finite-Difference. Time-Domain Method, Third Edition

## Slide 12: Finite-Difference Time-Domain
The Yee Algorithm
  Leapfrog method
  Input initial values at
  No need to solve simultaneous equations as and are known when needed
Taflove, Allen and Hagness, Susan C. Computational Electrodynamics: The Finite-Difference
Time-Domain Method, Third Edition

## Slide 13: Finite-Difference Time-Domain
Using central finite difference operator we can approximate first order derivatives
Can apply this process to all derivatives

## Slide 14: Finite-Difference Time-Domain
Partial derivative approximations are then used in the six equations:
Update equations for each field component can then be found and run in code

## Slide 15: Numerical Stability
The grid size and time step variables need to be chosen to satisfy S (stability factor)
  Choosing dimensions depends on the problem
  Need balance between accuracy and computation speed
  Major limitation is computational requirements, they increase very rapidly with finer grid sizes

## Slide 16: Phase Errors
Velocity Anisotropy Error
Wave has different phase velocity depending on their direction
Effects greatly reduced by using other algorithms or more samples per wavelength
Always a problem for larger simulation spaces

## Slide 17: Phase Errors
Physical Phase Velocity Error
  Phase lead or lag that is picked up when wave passes through a cell at a given angle
  Accumulates as wave propagates
                Easy to take into account in straight lines, not so much in complicated problems
                Is a function of the time sampling chosen; more samples, less error

## Slide 18: FDTD Simulation
Initial version implemented in Java using Processing[1] for graphics for quick development time
FDTD simulation features implemented so far…
  2D TM and TE polarisations
  Perfectly matched layers for boundary absorption
  Ability to model materials with specified permittivity, permeability and conductivity
  Plane wave/Gaussian beam source injection
Tested to work for total internal reflection, reflection and transmission coefficients, Brewster's angle, basic diffraction, etc.
[1] Processing Library – www.processing.org

## Slide 19
Gaussian Beam
Phase probes
3 mode grating

## Slide 21: Waveguide Coating
Thin grating layer of Ta2O5 applied to surface of a substrate
Can adjust the grating parameters and depth to get potentially 100% reflectivity at 1064nm
This setup is also suggested to be immune to the phase noise seen previously
Bunkowski et al.(2006)

## Slide 22
Steady state reached
Approx 1000 time steps
Simulation size 7.5um x 20um, processing time approx 300s
Si02
Ta2O5

## Slide 23: Waveguide grating - Preliminary
Only 40x16 samples done for this output, needs many more samples for more accurate graph
Minimum TE transmission at fill factor and grating depth
Minimum TM transmission at fill factor and grating depth

## Slide 24: Waveguide Grating - Preliminary
Only 40x40 samples done for this output, again more samples needed to find lower transmissions

## Slide 25: Waveguide Grating - Preliminary
Comparing to A. Bunkowski et al. (2006)
TM reflectivity results.
Low transmissions are comparable to high reflectivity seen from RCWA computations

## Slide 26: Conclusion
What has happened so far:
  Initial implementation of 2D FDTD simulation has been developed in Java and running on Beowulf cluster
  FDTD method appears to be a suitable method for simulating grating movements and the phase noises
  Shown that the ray picture phase noise also occurs in FDTD simulations of TEM00 diffraction
  Have begun to model the waveguide coatings, but some issues that need looking into

## Slide 27: Conclusion
Future plans:
  More work on verifying what is seen in FDTD simulations to the RCWA method used by A.Bunkowski et al. (2006)
  Measure the more relevant reflection coefficient for waveguide coatings and determine if it is immune to phase noises from moving grating
  Looking into isotropic dispersion techniques and how they can improve the simulation errors
  To further develop the tool for optical simulations