## Slide 1: Active Seismic Isolation in GEO
Holger Wittel
14.12.2010

## Slide 2: Motivation
Recently increased seismic activity at GEO during day time
Lock losses
Try to reinstate active seismic isolation system

## Slide 3: Silent night ...
Strong seismic transients even at nighttime!

## Slide 4
GEO
gravel mine 1
gravel mine 2

## Slide 5: The bad guys

## Slide 6: Seismic isolation
Good seismic isolation through triple pendulum + rubber stacks at high frequencies (> resonance at a few Hz)
Enough loop gain at low frequencies (<1Hz)
More suppression around 1 Hz possible?
(still local control dampening there)
Use piezos for active seismic isolation

## Slide 7: Ingredients for active seismic isolation
PZT stacks with max range of 25µm
Geophones on top of the PZTs
(for checking the performance)
STS2 seismometer next to the vacuum tanks
as input for the feed forward

## Slide 8: The stacks
Rubber stack
PZTs & geophones

## Slide 9: PZTs broken?!
Geophones show no response to PZT injections
Alternative:
act on the
foundation

## Slide 10: Shaking the foundation of GEO
Hydraulic shaking of the foundation
Take crowbar first

## Slide 11: Relief
More thorough investigation revealed:
The piezos are ok.
Proceed with piezo seismic isolation system,
beam splitter only for now

## Slide 12: Feed forward?
Stable
Simple
Geophones not good below 2 Hz
Image taken from J R Smith: Feedforward correction of mirror misalignment fluctuations for the GEO600 gravitational wave detector

## Slide 13: Broadband feed forward

## Slide 14: Transfer function STS2-> geophone

## Slide 15: Narrowband ff
We only care about the resonances at 0.55, 1.2 and 2.2 Hz
Make good transfer functions for those frequencies
Narrow bandpass:
right phase and gain at one frequency

## Slide 16: 0.55Hz feed forward

## Slide 17: 2.2Hz feed forward

## Slide 18: Summary
PZT feed forward works and provides suppression of the ambient seismic.
Transfer functions are a good meassure of performance.
Check the cables!
The broadband solution has better suppression than the narrowband ones, it is working at too high frequencies though.

## Slide 19: Outlook
Shifted broadband ff
More playing with filters
If necessary:
Upper mass ff
Spot position sensing
Optical lever